## Slide 1: A Dynamical Systems Approach to Neuromorphic Computation of Conditional Probabilities
Nigel Stepp (presenter) & Aruna Jammalamadaka
ndstepp@hrl.com
Information & Systems Sciences Laboratory
HRL Laboratories
Malibu, CA

## Slide 2: Why Neuromorphic Bayesian Inference?
?
?
?
?
Learning
Phase
“What if” questions about part replacement
“What if” questions about control actions
Probabilistic prediction of events for current conditions
Complicated System
Interactions Known
Readout Phase
Need to measure probabilistic data and perform probabilistic computations.
Applications like Fault Diagnostics must be Scalable and Efficient.

## Slide 3: Spike-Timing Dependent Plasticity
Spikes (and STDP) allow for very small computations
Spike-Timing Dependent Plasticity (STDP):
Connections that cause correlated spikes are strengthened
Connections that cause uncorrelated spikes are weakened
Computations occur due to single spikes, on the order of a few milli- or even microseconds.
A
B
“Pre” neuron
“Post” neuron
Time
+
+
-
-

## Slide 4: Developing a Probabilistic Computation Unit (PCU)
As an initial step, we want to show that synaptic weights in the Latigo chip can model the conditional probability between two random variables
Hypothesis: STDP and spike delays combine to create a conditional probabilistic computation unit
We want synaptic weight w to converge to a value p
i.e. we want w updates to have a fixed-point at p
A causes B to spike, resulting in an increase to w
We want STDP to implement a simple dynamical system

## Slide 5: Developing a Probabilistic Computation Unit (PCU)
As an initial step, we want to show that synaptic weights in the Latigo chip can model the conditional probability between two random variables
Hypothesis: STDP and spike delays combine to create a conditional probabilistic computation unit
If C spikes, delay will cause B to spike before A; causing w to decrease.
A will not cause B to spike due to a refractory period
Delayed feedback leads to exponential decay

## Slide 6: Developing a Probabilistic Computation Unit (PCU)
As an initial step, we want to show that synaptic weights in the Latigo chip can model the conditional probability between two random variables
Hypothesis: STDP and spike delays combine to create a conditional probabilistic computation unit
Now B will cause C to spike twice
- Once through D (fast path)
- Once through E (slow path)
Result: w decreases in proportion to itself
Delayed feedback leads to exponential decay

## Slide 7: Developing a Probabilistic Computation Unit (PCU)
As an initial step, we want to show that synaptic weights in the Latigo chip can model the conditional probability between two random variables
Hypothesis: STDP and spike delays combine to create a conditional probabilistic computation unit
Forcing A→B and inhibiting the decay path adds back a growth term
Combination of exp. decay and constant growth results in a stable fixed-point at a location we control

## Slide 8: Weight Decay Mechanism

## Slide 9: Probabilistic Computation Unit (PCU)
The synaptic weight w converges to a “fixed-point” at P(Y|X) by leveraging Spike Timing Dependent Plasticity (STDP), and delayed feedback
The PCU models the following differential equation
Where IT is the Tonic input and IP is the Phasic input.
Solving for w gives
Which converges exponentially to (in our case ) as
The output spikes of neuron D can either be decoded to convert the answer back into the probability domain, or fed into another neural network for subsequent computations
PCU

## Slide 10: Results with Hardware Restriction
Red = P(Y|X) ground truth probability used for synthetic data generation, Green = Estimate of actual P(Y|X) spikes fed into the PCU, Blue = weight values
Current implementation shows some saturation

## Slide 11: Composition and Scaling of PCUs
We can connect this functional unit to form networks
The networks learn conditionals in first stage
In second stage, weights are fixed and we can read out various conditionals
Modular composition enables neuromorphic compiler
M
x
y
z
C
x
z
y
=
C
M
C
M
M
X
Y
Z
P(Y|X) P(X|Z)
C
M
The functional unit can be compiled into networks for higher order computations

## Slide 12: Structure Learning
Using a fully-connected network of PCUs, conditional structure can be extracted from data
Bayesian Graphical Model
Learned Conditionals
Learned Transitive Closure

## Slide 13: Fault Diagnostics - Simulation
Using 6 simulated fault sources, learn conditional probability structure:
For readability, only faults 1 and 4 against others
Identifies conditional dependence over time
Demonstrates inherent smoothing ability
Method has also been applied to real aircraft fault messages
Time series for P(6|1)
Synaptic weights track conditional structure

## Slide 14: Thank You